## Slide 1
The fetch-decode-execute cycle, including its effect on registers
Structure and function of the processor
Role play (needs to be done in an open space): give each student in the class a role:
Program Counter Memory Address Register Memory Data Register Current Instruction Register Accumulator Address bus Control bus Data bus Decode Unit Memory Read Signal Memory Write Signal
Memory address 0001
Memory address 0010
Memory address 0011
Memory address 0100
Memory address 0101
Memory address 0110
Memory address 0111
If necessary, the memory addresses can be fewer students if the class is small. If it is larger, some students can be the actual binary flowing through the system.

## Slide 2
The fetch-decode-execute cycle, including its effect on registers
Structure and function of the processor
The students each have one of the printed slides according to their role.
They should arrange themselves in the open space so they match an abstracted view of the structure of the processor, buses and RAM. e.g. the program counter needs to be close to the memory address register.
The student with the program counter, accumulator and memory locations will also need some additional blank sheets and a marker pen so they can show a change their registers, or pass a copy of their values on.

## Slide 3
The fetch-decode-execute cycle, including its effect on registers
Structure and function of the processor
The teacher passes the address of the first instruction to the student representing the program counter.
That student would pass the address to the memory address register, and on one of their blank sheets of paper write the address of the next instruction (incremented from the previous value) to keep for the next cycle.
The students then act out the fetch-decode-execute cycle, passing the relevant information to each student.
The teacher will need to play the role of the system clock and control unit, co-ordinating the role play!
The program should add the numbers 2 and 3, storing the answer 5.
The program uses direct addressing where the address of the data is in the operand of the instruction.

## Slide 4
PROGRAM COUNTER
I am a register in the CPU. I hold the address of the next instruction to be fetched.

## Slide 5
MEMORY ADDRESS REGISTER
I am a register in the CPU. I hold the address of the next instruction from the program counter or current instruction register.

## Slide 6
MEMORY DATA REGISTER
I am a register in the CPU. I hold the data or instruction that is sent along the data bus.

## Slide 7
CURRENT INSTRUCTION REGISTER
I am a register in the CPU. I hold the instruction executing. I am connected to the memory data register and the memory address register.

## Slide 8
ACCUMULATOR
I am a register in the CPU. I work for the arithmetic logic unit with the current instruction register.

## Slide 9
ADDRESS BUS
I am a bus connecting the CPU and memory. I send the address of the instruction or data to be fetched from the memory address register to the memory.

## Slide 10
CONTROL BUS
I am a bus connecting the CPU and memory. I send memory read and memory write commands to the memory.

## Slide 11
DATA BUS
I am a bus connecting the CPU and memory. Instructions and data travel along me between the CPU and memory. I am connected to the memory data register.

## Slide 12
DECODE UNIT
I am a component of the CPU. I am connected to the current instruction register.
These are the instructions I understand:
0000 0000 end
0001 xxxx add xxxx to accumulator
0010 xxxx subtract xxxx from accumulator
0011 xxxx store accumulator in memory address xxxx
0101 xxxx load contents of address xxxx to accumulator
0110 xxxx change program counter to xxxx

## Slide 13
MEMORY READ SIGNAL
I am a signal sent from the control unit along the control bus to the memory:

## Slide 14
MEMORY WRITE SIGNAL
I am a signal sent from the control unit along the control bus to the memory:

## Slide 15
MEMORY ADDRESS 0001
0101 0101
I am a memory address. My contents travels down the data bus if I get a memory read signal. I overwrite my data with what comes from the data bus if I get a memory write signal.

## Slide 16
MEMORY ADDRESS 0010
0001 0110
I am a memory address. My contents travels down the data bus if I get a memory read signal. I overwrite my data with what comes from the data bus if I get a memory write signal.

## Slide 17
MEMORY ADDRESS 0011
0011 0111
I am a memory address. My contents travels down the data bus if I get a memory read signal. I overwrite my data with what comes from the data bus if I get a memory write signal.

## Slide 18
MEMORY ADDRESS 0100
0000 0000
I am a memory address. My contents travels down the data bus if I get a memory read signal. I overwrite my data with what comes from the data bus if I get a memory write signal.

## Slide 19
MEMORY ADDRESS 0101
0000 0010
I am a memory address. My contents travels down the data bus if I get a memory read signal. I overwrite my data with what comes from the data bus if I get a memory write signal.

## Slide 20
MEMORY ADDRESS 0110
0000 0011
I am a memory address. My contents travels down the data bus if I get a memory read signal. I overwrite my data with what comes from the data bus if I get a memory write signal.

## Slide 21
MEMORY ADDRESS 0111
0000 0000
I am a memory address. My contents travels down the data bus if I get a memory read signal. I overwrite my data with what comes from the data bus if I get a memory write signal.

## Slide 22
0001
Address of the first instruction to pass to program counter at the start of the role play.